## Slide 1: COSC 6376 Project An Investigation into AWS File Systems (EC2 and S3)
Daniel Fernandez
Glenn Turner

## Slide 2: Motivation
No experience
Block Storage
vs
Object Storage
Elastic Block Store
Simple Storage Service
Data Storage
is critical
Notes: 1. “No experience with storage services presented in class”
2. “Amazon Web Services has a bewildering collection of file system choices”
“AWS offers many choices. We focused on 2 of their storage services”
3. “These seem to be interesting and possibly new ways of manipulating data in storage.”

## Slide 3: Experimental Apparatus
Simulate actual work conditions
Fairly large amount of IO operations
Control over the record size.
File systems on most computers are block devices.
  Naïve: Hoped that EBS may offer some additional IO capability.
  Additionally, retrieving blocks of storage, as objects, by an identifier seems appealing.
Notes: IO operations:
- Write: 2.4+ million records
- Read: 215,000 records
Record sizes: BLOCKSIZE, LRECL, DRECL

## Slide 4: Experimental Data
List of registered voters in Harris County (obtained via FOIA request)
  2.48 Million records
  In apparent random order
List of voters in the county election of 2021
  In-person & Mail-in voting
  Data in order of votes received (apparent random order)
  Used a sample of 215,000 of these voters.

## Slide 5: Constructing the Database
Registered voter list: csv file (2.48 Million records).
Python dictionary: Built to keep track of where records are stored.
Key: Voter ID
Value: (Block number, Offset)
Block Storage:
Records are padded
Records embedded into larger physical records
Object Storage:
Records are not padded
1+ voter records embedded into objects
Notes: “padded to a predetermined length”
“the location of the data record as a physical record number and the offset into that physical record. “

## Slide 6
Dictionary Entries
Data Entry
The binary physical records are all the same size.
This is a program parameter.
The Data Records
To save the dictionary the entries are written into the physical records.
Part of the experiments conducted was to examine the size of the physical records

## Slide 7: Operations we examined in EBS
Build the Database
  Build dictionary
  Write dictionary
  Build Database
Using the Database
  Read dictionary from file
  Fetch records in the Database
Notes: Fetch records in the database “according to our sample of 215,000 voters (that voted in 2021 Harris county election)”
Build Dictionary and read dictionary from file seem to be slow irrespective of disk speed, they are probably compute intensive due to creating hash codes

## Slide 8: First Results
Chart: WSL Test Run Times in seconds
| 512 | 2048 | 4096 | 8192 | 16384 | 32768
build dict | 2.6898 | 2.6916 | 2.6766 | 2.6698 | 2.6982 | 2.6692
write dict | 2.7734 | 2.7368 | 2.7734 | 2.758 | 2.7496 | 2.642
build database | 2.4562 | 2.3324 | 2.3308 | 2.246 | 2.2152 | 2.1702
read dict from file | 2.9254 | 2.8712 | 2.88 | 2.9172 | 2.912 | 2.9096
fetch records | 0.8378 | 0.8606 | 0.8256 | 0.8884 | 1.0272 | 1.281
Chart: T2 Micro Times in Seconds
| 128 | 512 | 2048 | 4096 | 8192 | 16384
build dict | 5.2573 | 5.3167 | 5.1785 | 5.1967 | 5.2373 | 3.9385
write dict | 4.8767 | 5.1167 | 5.154 | 5.0961 | 5.1113 | 4.8559
build database | 5.62 | 5.0332 | 4.8314 | 4.7763 | 4.6841 | 4.6152
read dict from file | 6.0942 | 6.0962 | 6.0154 | 6.0262 | 6.0602 | 5.9375
fetch records | 5.7717 | 6.2568 | 5.4442 | 5.3798 | 5.6402 | 6.0895
Notes: What to beat

## Slide 9: Instance Types Tested
Designation | Characteristics | Cost
t2 micro | 1 Core, 1 thread,1 GB , 2.5 GHz, 1 MB | Free
t3 large | 1 core, 2 threads, 8 GB, 2.5 GHz, | $0.0832 /hr
d3 xlarge | 2 cores, 4 threads, 32 GB, 2.5 GHz | $0.499 / hr
I4 xlarge | 2 cores, 4 threads, 32 GB, 2.9 GHz | $0.343 / hr

## Slide 10: Different Instance Types
This is the most compute intensive task for various instance types
* With a physical record size of 4096
Chart: Time to Build Dictionary
| 512 | 4096 | 32678
t2 micro | 5.5618 | 5.4916 | 5.1882
t3 large | 4.5595 | 4.5784 | 4.525
d3 xlarge | 4.118 | 4.1032 | 4.0879
i4 xlarge | 3.2713 | 3.244 | 3.253

## Slide 11: Disk Types Tested
Designation | Measured Speed | Size
GP2 | 81.3 MB /sec | 8 GB
GP3 | 260 MB /sec | 
IO2 | 330 MB /sec | 10 GB*
D3 | 181 MB /sec | 1.8 TB**
I4 xlarge (Nitro) | 1050 MB / sec | 800 GB**
When Creating an instance the size and type of volume to go with it are selectable with these exceptions
* The 1.8 TB disk is added automatically
**This is a secondary disk automatically added

## Slide 12: Different Disk Types
This is randomly retrieving the records T3 large
The keys are stored in an array, so there is no other IO
Chart: Random Access IO
| 512 | 4096 | 32768
gp2 | 1.0417 | 1.194 | 1.9949
gp3 | 1.0434 | 1.17 | 1.9954
io2 | 0.9894 | 1.1425 | 1.9087

## Slide 13: Different Disk Types
This is randomly retrieving the records
This reading key file
Chart: Random IO while reading keys
| 512 | 4096 | 32768
t3 io2 | 1.0905 | 1.2575 | 2.015
D3 | 1.2351 | 1.2037 | 2.1371
i4 (nitro) | 0.75616 | 0.85816 | 1.4288

## Slide 14: Best Results
Chart: WSL Test Run Times in seconds
| 512 | 2048 | 4096 | 8192 | 16384 | 32768
build dict | 2.6898 | 2.6916 | 2.6766 | 2.6698 | 2.6982 | 2.6692
write dict | 2.7734 | 2.7368 | 2.7734 | 2.758 | 2.7496 | 2.642
build database | 2.4562 | 2.3324 | 2.3308 | 2.246 | 2.2152 | 2.1702
read dict from file | 2.9254 | 2.8712 | 2.88 | 2.9172 | 2.912 | 2.9096
fetch records | 0.8378 | 0.8606 | 0.8256 | 0.8884 | 1.0272 | 1.281
Chart: I4 Xlarge Time in Seconds
| 512 | 2048 | 4096 | 8192 | 16384 | 32768
Build Dict | 3.2713 | 3.258 | 3.244 | 3.2312 | 3.2535 | 3.253
Write dict | 2.9649 | 3.3478 | 3.0391 | 3.0519 | 3.0275 | 3.0286
Build Database | 2.7698 | 2.5453 | 2.515 | 2.4686 | 2.4355 | 2.4087
Read Dict | 3.733 | 3.5632 | 3.6661 | 3.6358 | 3.6493 | 3.6267
Fetch Records | 0.75616 | 0.80832 | 0.85816 | 0.9399 | 1.0983 | 1.4288
Notes: What to beat

## Slide 15: AWSCLI Setup

## Slide 16: EBS Challenges
We didn’t see a lot of difference in the GP2 GP3 and IO2 disks. The disks used in the “I” family are faster.
The expense is non-trivial. Daily use for a single user would rival or surpass purchase of a desktop computer.

## Slide 17: EBS Challenges in Testing
When creating an instance the region may be selected but the Availability zone is not. Volumes may be selected in an Availability zone. A volume created may not be made available to another instance.

## Slide 18: S3 Challenges

## Slide 19: Contributions

## Slide 20
Thank You